## Slide 1: ARC EM Starter Kit (v2.2) Introduction

## Slide 2: Agenda
ARC EM Starter Kit Overview
ARC FPGA design
Introduction to on-board device
Programmer’s reference
Getting started

## Slide 3: ARC EM Starter Kit
ARC EM Starter Kit is a low-cost, versatile solution enabling rapid software development, code porting, software debugging, and profiling for ARC EMxD processors. It consists of:
Hardware platform, including pre-installed FPGA images of ARC EM7D, EM9D & EM11D configurations with peripherals
embARC Open Software Platform gives developers online access to device drivers, application examples and a suite of free and open-source software that speeds software development for ARC-based embedded systems
Robust ecosystem of development tools & software including Synopsys ARC MetaWare Development Toolkit, and open source ARC GNU

## Slide 4: Board Package
ARC EM Starter Kit package contains the following items:
    FPGA module with Xilinx Spartan-6 XC6SLX150-3FGG484C FPGA device mounted on base board with extension connectors and peripherals
    4-channel 12-bit A/D converter extension module
    100-240V AC power adapter
    USB cable
    ARC EM Starter Kit Getting Started document
    PmodTMP2 Thermometer

## Slide 5: Board Overview
The ARC EM Starter Kit consists of two boards:
FPGA module with a Xilinx Spartan-6 XC6SLX150-3FGG484I FPGA device
Base board with extension connectors and peripherals
The kit has the following on-board peripheral devices:
  2×16-bit-wide 1 Gbit (128 MB) DDR3 SDRAM
  128 Mbit (16 MB) SPI Flash memory
  SD card reader
  Push-buttons and LEDs
  DIP switches
  Seven Pmod connectors for device extension
  JTAG and serial console over USB
  Standard 20-pin JTAG connector also supporting 4-wire JTAG for ARC EM processor
  On-board clock oscillator

## Slide 6: Agenda
ARC EM Starter Kit Overview
ARC FPGA design
Introduction to on-board device
Programmer’s reference
Getting started

## Slide 7: FPGA Design Overview
HW architecture of the FPGA design implemented in the ARC EM Starter Kit

## Slide 8: EM Configurations
The FPGA board SPI flash storage device is pre-installed with 3 FPGA images with different configurations of ARC EM cores, one image can be selected to program FPGA by board settings
  ARC_EM7D
  ARC_EM9D
  ARC_EM11D
Parameters | Configurations |  | 
 | ARC_EM7D | ARC_EM9D | ARC_EM11D
ICCM | 256 KB | 256 KB | 64 KB
DCCM | 128 KB | 128 KB | 64 KB
DDR3 | 128 MB | 128 MB | 128 MB
Instruction Cache | 16 KB | - | 16 KB
Data Cache | 16 KB | - | 16 KB
Timers | 2 | 2 | 2
Address width | 32 | 32 | 32
DSP | complex | complex, itu, accshift | complex, itu, accshift
XY memory | - | DCCM+X+Y, 8K | DCCM+Y, 8K
FPU | - | Single precision | Single & Double
Fmax | 30MHz | 20MHz | 20MHz
SW1 DIP switch settings (Bit0, Bit1) | (OFF, OFF) | (ON, OFF) | (OFF, ON)
The FPGA image is selected with pins 1 and 2 of the SW1 DIP switch on the base board

## Slide 9: Peripheral Controllers
In addition to ARC EM core, every FPGA image includes a set of DesignWare peripheral controllers connected to the on-board devices and external interfaces via pin-sharing logic
  UART
  GPIO
  I2C
  SPI master
  SPI slave
  Timers & WDT
General information about DesignWare components can be found at
http://www.synopsys.com/IP/Pages/default.aspx
  DW_apb_uart – Universal Asynchronous Receiver/Transmitter
  DW_apb_gpio – General Purpose Programmable I/O
  DW_apb_i2c – I2C interface
  DW_apb_ssi – Synchronous Serial Interface (SPI)
  DW_apb_wdt – WDT
  DW_apb_timers – Timers

## Slide 10: Peripheral-GPIO
This IP controls push buttons, LEDs, DIP switches and provides the GPIO functionality of the Pmod connectors. GPIO have the following 4 ports
  Port A width is 32 bits
  Port B width is 9 bits
  Port C width is 32 bits
  Port D width is 12 bits
Port A includes debounce logic and supports interrupt processing. It generates a single, combined interrupt connected to the ARC EM interrupt controller port irq_22

## Slide 11: Peripheral-UART
FPGA design includes three separate ports
  UART0 is connected to the external interfaces via pin-sharing logic. It can optionally be accessed at the Pmod1 connector
  UART1 is internally connected to an on-board UART-to-USB converter and used as default console for demo applications
  UART2 is connected to the external interfaces via pin-sharing logic. It can optionally be accessed at the Pmod5 connector
DW UART 0
DW UART 2
ARC
core
Pmod1
USB
UART
CTS
RTS
RXD
TXD
CTS
RTS
RXD
TXD
DW UART 1
Pin MUX
Pmod5
RTS
RXD
TXD
CTS
UART
MUX

## Slide 12: Peripheral-SPI Master
The SPI Master has 6 chip select outputs, can control up to 6 SPI devices
  On-board SPI flash memory
  On-board SD Card
  Internal SPI Slave
  Up to 3 SPI peripherals connected to Pmod connectors
ARC
core
SCK
SDO
SDI
CS5
CS4
CS3
CS0
CS1
CS2
DW
SSI master
Pin
MUX
Pmods
SD Card
SPI
Slave
SPI
Flash

## Slide 13: Peripheral-SPI Slave
SPI slave can be
  Connected to the external interface via pin-sharing logic and can optionally be accessed at the Pmod1 connector
  Connected to the SPI Master inside the FPGA using CS4 for test purposes only

## Slide 14: Peripheral-I2C
I2C can be programmed at run-time either as a master or a slave device. It supports I2C standard and fast mode (up to 400 kHz). Master mode allows multiple I2C slaves to be connected
It is connected to the external interfaces via pin-sharing logic and can optionally be accessed at the connectors Pmod2 and Pmod4. The PmodAD2 extension board, provided with the ARC EM Starter kit, connects to the main board using the I2C interface
ARC
core
DW I2C 0
Pin
MUX
PMOD 2
PMOD 4
SCL
SDA
DW I2C 1
Pin
MUX
SCL
SDA
SCL
SDA
SCL
SDA

## Slide 15: Pin Mux Controller
The Pin Mux Controller connects the peripheral controllers to the external hardware interfaces and to each other
Offset | Register Name | Default value | Description
0x0 | PMOD_MUX_CTRL | 0X0 | This register controls mapping of the peripheral device signals on Pmod connectors. Refer to the Pmod Pins Configuration section for more details
0x4 | I2C_MAP_CTRL | 0X0 | Reserved for future extensions.
0x8 | SPI_MAP_CTRL | 0X0 | SPI_MAP_CTRL[0] selects the mode of operation of the SPI slave: Normal operation, SPI_MAP_CTRL[0]=0: SPI slave is connected to Pmod1 at connector J1. Loop-back mode, SPI_MAP_CTRL[0]=1: SPI slave is connected to the SPI master inside the FPGA using CS4. This mode is for test purposes only. This register is ignored for ARC_EM6 and ARC_EM6_GP configurations.
0xc | UART_MAP_CTRL | 0XE4 | This register controls the mapping of the UART signals on the Pmod1 connector. Refer to the Pmod Pin Configuration section for more datails.
0x14 | SPI_MST_CS_CTRL | 0X0 | SPI Master select control.

## Slide 16: System Clock
The Peripheral Controllers uses a system clock and a peripheral clock for the interface
Components | System clock EM7D/EM9D/EM11D | Peripheral clock
CPU/Timer | 30MHz/30MHz/20MHz | -
GPIO | 30MHz/30MHz/20MHz | -
UART | 30MHz/30MHz/20MHz | 50MHz
SPI Mater | 30MHz/30MHz/20MHz | 50MHz
SPI Slave | 30MHz/30MHz/20MHz | 50MHz
I2C | 30MHz/30MHz/20MHz | 50MHz
The table lists the clocks used by different peripheral interface

## Slide 17: Memory Map and Interrupts
Interrupt | Component
irq_22 | GPIO controller
irq_23 | I2C_0 controller
irq_24 | I2C_1 controller
irq_25 | SPI Master controller
irq_26 | SPI Slave controller
irq_27 | UART0
irq_28 | UART1
irq_29 | UART2
irq_30 | WDT
irq_31 | DW Timer 0
irq_32 | DW Timer 1
EM7D
EM9D
EM11D

## Slide 18: Agenda
ARC EM Starter Kit Overview
ARC FPGA design
Introduction to on-board device
Programmer’s reference
Getting started

## Slide 19: On Board Device
JTAG Connector(J15)
  It is recommended to use the USB interface for JTAG debugging. Alternatively, it is possible to use industry-standard debug probes connected to the 20-pin JTAG
USB(J7) is used for several purposes
  ARC JTAG debugging port
  UART debug console
  FPGA bit file programming
SD Card
  The SD card interface works in SPI mode
Man-Machine Interface
  Push Buttons, LEDs
  DIP-Switches, Jumpers
Pmod connectors(J1-J6, J20)
  Pmod connectors are used to connect external hardware interface devices with ARC EM Starter Kit

## Slide 20: Device and Peripheral
Peripherals | Board connection
GPIO Port A[2:0] | Buttons: [Above letter ‘A’ in ARC logo, L,R]
GPIO Port A[31:8] | Pmods J1, J2, J3, J4, J5, J6, [10:7] pins
GPIO Port B[8:0] | LEDs[8:0] Port B[0] controls LED0 Port B[1] controls LED1 … Port B[8] controls LED8 The LED is on if its corresponding control bit is programmed to ‘0’
GPIO Port C[3:0] | DIP Switch SW1 SW1 switch 1 connected to Port C[0] SW1 switch 2 connected to Port C[1] SW1 switch 3 connected to Port C[2] SW1 switch 4 connected to Port C[3]
GPIO Port C[31:8] | Pmods (J1, J2, J3, J4, J5, J6) [4:1] pins
GPIO Port D[11:0] | Pmods J4, J20

## Slide 21: Device and Peripheral (2)
Peripherals | Board connection
I2C_0 | Pmod J2
I2C_1 | Pmod J4
SPI Master CS0 | Pmods J6 [4:1] pins
SPI Master CS1 | Pmods J5 [4:1] pins
SPI Master CS3 | SD Card
SPI Master CS4 | Internal loopback to SPI Slave when register SPI_MAP_CTRL[0]=1
SPI Slave | Pmod J1 [10:7] pins when SPI_MAP_CTRL[0]=0 Internal loopback to SPI Master when SPI_MAP_CTRL[0]=1 (for test purposes)
UART 0 | Pmod J1 [4:1] pins
UART 1 | USB UART (debug console)
UART 2 | Pmod J5 [10:7] pins

## Slide 22: Pmod Connectors
External hardware interface devices can be connected to the ARC EM Starter Kit using Pmod connectors. The table below provides an overview of possible peripheral combinations for each Pmod connector
The functionality of the Pmod connectors is programmable. Each connector can operate either as a GPIO or as a dedicated peripheral device
Pmod bits [5] and [11] are connected to GND
Pmod bits [6] and [12] are connected to 3.3V
Pmod bits [4:1][10:7] are functional pins
These connectors comply with the Pmod Interface Specification by Digilent Inc
Pmod | Pmod connector | Peripherals | 
 |  | MUX option 0 | MUX option 1
Pmod1 | J1 | GPIOs | External SPI master + UART0
Pmod2 | J2 | GPIOs | ARC EM control/status signals + I2C0
Pmod3 | J3 | GPIOs | Reserved
Pmod4 | J4 | GPIOs | GPIO + I2C1
Pmod5 | J5 | GPIOs | External SPI slave 1 and UART2
Pmod6 | J6 | GPIOs | External SPI slaves 0 and CS outputs for all other SPI slaves + ARC EM control/status signals
Pmod7 | J20 | GPIOs | ARC EM control/status signals

## Slide 23: Pmod™ Compatible Extensions
Pmods™ are small I/O interface boards that offer an ideal way to extend the capabilities. Pmods include sensors, I/O, data acquisition & conversion, connectors, external memory, and more
"Pmod™" is the trademark of Digilent Inc. The Pmod Interface Specification is the property of Digilent Inc.

## Slide 24: Pmod Device DIY
SPI interface
SPI-based Pmod example
Order modules on Taobao/Amazon/….
Get module pins description & Pmod SPI Interface standard
Use flying wire to connect module pins to corresponding pins of Pmod connector

## Slide 25: Pmod Pin Configuration
Pmod1 configuration:
  Set PM1[0] = 0 – Pmod1[4:1] are connected to DW GPIO Port C[11:8]
  Set PM1[0] = 1 – Pmod1[4:1] are connected to DW UART0 signals.
  Set PM1[2] = 0 – Pmod1[10:7] are connected to DW GPIO Port A[11:8].
  Set PM1[2] = 1 – Pmod1[10:7] are connected to DW SPI Slave signals.
Note: PM1[1] and PM1[3] are reserved
Pmod pins are configured by the Pin Mux Controller via the PMOD_MUX_CTRL register
Reserved | PM7[1:0] | PM6[3:0] | PM5[3:0] | PM4[3:0] | PM3[3:0] | PM2[3:0] | PM1[3:0]
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
PMOD_MUX_CTRL register
Default value: 0X0
Pmod1 pins (J1) | PM1[2]=0 | PM1[2]=1
 | GPIO Signals | SPI signals
10 | Port A [11] | SCLK_S
9 | Port A [10] | MISO_S
8 | Port A [9] | MOSI_S
7 | Port A [8] | CS_S_N

## Slide 26: PmodAD2 Extension Module
Here are an example shows how the PmodAD2 should be connected to Pmod
  The PmodAD2 module is a 4-channel 12-bit A/D converter with a Pmod I2C interface(a 2x4 pin Pmod connector)
  Insert the module on the left side of connector J2, J3 or J4 using pins 3, 4, 5, 6, 9, 10, 11, 12.
To operate the Pmod connector in I2C mode, set the PMOD_MUX_CTRL register as follows
  PM2[0] = 1 (for Pmod2 at J2)
  PM3[0] = 1 (for Pmod3 at J3)
  PM4[0] =1 (for Pmod4 at J4)

## Slide 27: Agenda
ARC EM Starter Kit Overview
ARC FPGA design
Introduction to on-board device
Programmer’s reference
Getting started

## Slide 28: Simple Application
Application code named myhello.c
Compile your application
ccac myhello.c -av2em -core1 -Os -Hpfnoflt -Hldopt=-Bbase=0x100 -o myhello.elf
Run your application in MetaWare command line mode
mdb -cl -run -hard -digilent myhello.elf
#include "stdio.h"
int main(void) {
printf("Hello world");
return 0;
}
The “Hello world” message will be printed on desktop by MetaWare debugger via a Hostlink interface over a JTAG connection

## Slide 29: Simple Application (2)
Run your application in MetaWare GUI mode
mdb -run -hard -digilent myhello.elf
Set target as following:
Hardware
Digilent Jtag cable
4-wire(standard)

## Slide 30: Operating Modes
Developing and Debugging Code Using MetaWare Tools
  A user application can be loaded and debugged using the MetaWare debugger via a Hostlink interface over a JTAG connection, user can use all debug functionality provided by the MetaWare debugger, such as:
    Running in step by step mode
    Using breakpoints
    Variable watch
    Memory read/write
  Use the following command to run your application in the MetaWare debugger:
  mdb -run -hard -digilent <your-application>.elf

## Slide 31: Operating Modes
Running the Application in Self-boot Mode
Once the FPGA image is loaded, a bootloader program is placed inside the ICCM and executed. The bootloader behavior depends on bits 3 and 4 of the on-board DIP switch SW1
  Bit 4 – load executable image from SPI flash.
    When this bit is ON the startup code checks for the presence of an application stored in SPI flash and copies the application image to RAM. Next, it verifies the checksum and executes the application from the start address
  Bit 3 – affects the console output of the bootloader.
    Setting Bit 3 to the ON position suppresses console output. When Bit 3 is on the OFF position the bootloader prints the parameters of the self-boot image and indicates the status of the loading process

## Slide 32: Operating Modes-SPI Flash
The flash memory is divided in two sections: FPGA image and Application. The Application section contains the main code for the application and header, and the FPGA section contains the default core configurations for FPGA.
The header contains the following information
  Application image size
  RAM destination address
  Checksum
  Start address from which the
  CPU starts code execution after loading

## Slide 33: Agenda
ARC EM Starter Kit Overview
ARC FPGA design
Introduction to on-board device
Programmer’s reference
Getting started

## Slide 34: Getting Started
Connect USB cable between board and PC
Connect power supply
Follow links in quick start guide to install software
Run self-boot application
Run supplied example applications
Use examples as a starting point for your own application