## Slide 1: ARC Processor-Based Embedded Programming
Professor: Sci.D., Professor
Vazgen Melikyan

## Slide 2: Lecture 8: ARC IoT Development Kit

## Slide 3: Contents
ARC IoT Development Kit
ARC IoT SoC Introduction
On-board Device Introduction
Programmer’s Reference
Getting Started

## Slide 4: Contents
ARC IoT Development Kit
ARC IoT SoC Introduction
On-board Device Introduction
Programmer’s Reference
Getting Started

## Slide 5: ARC IoT Development Kit
The DesignWare® ARC® IoT Development Kit(ARC IoT DK) is a versatile platform that includes the necessary hardware and software to accelerate software development and debugging of sensor fusion, voice recognition, and face detection applications
Hardware platform includes a silicon implementation of the ARC Data Fusion IP Subsystem as well as a rich set of peripherals
embARC Open Software Platform gives developers online access to device drivers, application examples and a suite of free and open-source software that speeds software development for ARC-based embedded systems
Robust ecosystem of development tools & software including Synopsys ARC MetaWare Development Toolkit, and open source ARC GNU

## Slide 6: Target Applications
Target the following domains based on ARC EM9D processor
  IoT end nodes
  Sensor Fusion
  Low-power voice/audio
Easy to extend end-devices through available Arduino, mikroBus, and Pmod connectors
  Sensors
  Actuators
  Displays
  Buttons & Switches
  Communication devices

## Slide 7: Contents
ARC IoT Development Kit
ARC IoT SoC Introduction
On-board Device Introduction
Programmer’s Reference
Getting Started

## Slide 8: Overview of ARC IoT SoC
ARC IoT SoC Top-Level Diagram

## Slide 9: ARC IoT SoC Main Features
DesignWare ARC Data Fusion Subsystem
  EM9D Core at 144 MHz
      256 KB ICCM
      128 KB DCCM
      32 KB Xmemory
      32 KB Ymemory
      Memory Protection Unit
      DMA controller, FPU
  DSP accelerator functions
  Advanced power management - DVFS
      Clock and voltage switching. On-chip voltage switches for digital core logic supplies
      Off-chip voltage switches for all other supplies and DFSS tightly coupled peripherals
  4 x UART
  3 x SPI master
  1 x SPI slave
  3 x I2C master
  44 bit GPIO (4 x 8-bit + 3 x 4-bit)
128 KB SRAM
256 KB eFLASH (50 MHz read operation)
2 MB Boot SPI
Real Time Clock (RTC) running at 32.678 kHz
I2S TX/RX interface
SDIO interface (2x)
USB 2.0 OTG interface
JTAG interface for debug
PWM interface
  6 PWM channels
  2 PWM timers
    1 timer for channel 1/2/3 and 1 timer for channel 4/5/6
ADC interface, 16-channel single-ended 12-bit

## Slide 10: ARC IoT SoC Clock Architecture
16MHz reference clock for system clocks generation
Centralized clock generation
Single PLL and integer dividers
Allows for accurate fine-tuning of the system clocks to the desired frequency
Other input clocks
30MHz charge-pump clock for eFLASH
12MHz reference clock for USB
4.096 - 28.224MHz reference clock for audio
32.768khz standby clock

## Slide 11: Interrupt Overview
All the interrupts sources are routed directly to the ARC EM9D interrupt controller
Each interrupt can be enabled/disabled individually
Sensitivity can be re-programmed from level to edge
All interrupts are enabled and level sensitive after reset, active-high

## Slide 12: Interrupt Mapping
IRQ# | Interrupt Source | Remarks
Irq16 | timer0 | 
Irq17 | timer1 | 
Irq18 | Watchdog Timer | 
Irq19 | io_gpio | gpio_4b0_gpio_intr_flag
irq20 : irq35 | DMA controller | DMA_done[15:0]
irq36 : irq51 | DMA controller | DMA_err[15:0]
Irq52 | io_gpio | gpio_4b1_gpio_intr_flag
Irq53 | io_gpio | gpio_4b2_gpio_intr_flag
Irq54 | io_gpio | gpio_8b0_gpio_intr_flag
Irq55 | io_gpio | gpio_8b1_gpio_intr_flag
Irq56 | io_gpio | gpio_8b2_gpio_intr_flag
Irq57 | io_gpio | gpio_8b3_gpio_intr_flag
Irq58 | i2c_mst0 | i2c_mst0_iic_mst_intr_err
Irq59 | i2c_mst0 | i2c_mst0_iic_mst_intr_rx_avail
irq60 | i2c_mst0 | i2c_mst0_iic_mst_intr_tx_req
Irq61 | i2c_mst0 | i2c_mst0_iic_mst_intr_stop_det
Irq62 | i2c_mst1 | i2c_mst1_iic_mst_intr_err
irq63 | i2c_mst1 | i2c_mst1_iic_mst_intr_rx_avail
Irq64 | i2c_mst1 | i2c_mst1_iic_mst_intr_tx_req
Irq65 | i2c_mst1 | i2c_mst1_iic_mst_intr_stop_det
irq66 | i2c_mst2 | i2c_mst2_iic_mst_intr_err
Irq67 | i2c_mst2 | i2c_mst2_iic_mst_intr_rx_avail
Irq68 | i2c_mst2 | i2c_mst2_iic_mst_intr_tx_req
irq69 | i2c_mst2 | i2c_mst2_iic_mst_intr_stop_det
Irq70 | spi_mst0 | spi_mst0_spi_mst_err_intr
Irq71 | spi_mst0 | spi_mst0_spi_mst_intr_rx_avail
Irq72 | spi_mst0 | spi_mst0_spi_mst_intr_tx_req
irq73 | spi_mst0 | spi_mst0_spi_mst_intr_idle
Irq74 | spi_mst1 | spi_mst1_spi_mst_err_intr
Irq75 | spi_mst1 | spi_mst1_spi_mst_intr_rx_avail
irq76 | spi_mst1 | spi_mst1_spi_mst_intr_tx_req
irq77 | spi_mst1 | spi_mst1_spi_mst_intr_idle
IRQ# | Interrupt Source | Remarks
Irq78 | spi_mst2 | spi_mst2_spi_mst_err_intr
irq79 | spi_mst2 | spi_mst2_spi_mst_intr_rx_avail
Irq80 | spi_mst2 | spi_mst2_spi_mst_intr_tx_req
Irq81 | spi_mst2 | spi_mst2_spi_mst_intr_idle
irq82 | spi_slv0 | spi_slv0_spi_slv_err_intr
Irq83 | spi_slv0 | spi_slv0_spi_slv_intr_rx_avail
Irq84 | spi_slv0 | spi_slv0_spi_slv_intr_tx_req
Irq85 | spi_slv0 | spi_slv0_spi_slv_intr_idle
Irq86 | uart0 | uart0_uart_intr
Irq87 | uart1 | uart1_uart_intr
Irq88 | uart2 | uart2_uart_intr
Irq89 | uart3 | uart3_uart_intr
Irq90 | external | External wakeup interrupt
Irq91 | sdio | SDIO interrupt
Irq92 | i2s tx | I2S TX empty interrupt
Irq93 | i2s tx | I2S TX overrun interrupt
Irq94 | i2s rx | I2S RX data available interrupt
Irq95 | i2s rx | I2S RX overrun interrupt
Irq96 | USB | USB interface interrupt, Active low
Irq97 | adc_int | ADC convert channels finish interrupt
Irq98 | i_timer | i_timer interrupt[0]
Irq99 | i_timer | i_timer interrupt[1]
Irq100 | i_timer | i_timer interrupt[2]
Irq101 | i_timer | i_timer interrupt[3]
Irq102 | i_timer | i_timer interrupt[4]
Irq103 | i_timer | i_timer interrupt[5]
Irq104 | i_rtc | i_rtc interrupt

## Slide 13: Memory Map Overview
System Memory
  256 KB eFLASH
  2 MB Boot SPI
  128 KB SRAM
  256 KB ICCM
  128 KB DCCM
  32 KB XMemory
  32 KB YMemory
2 x 2 Mbyte SPI Flash
  One SPI Flash (U19, connected to the Boot SPI) is pre-loaded with a firmware upgrade application
  One SPI Flash (U35, connected to SPI master 0) is available for users
Offset | Size | Slave
0x0000_0000 | 256 KB | eFLASH READ
0x1000_0000 | 2 MB | External BOOT SPI Flash
0x2000_0000 | 256 KB | ICCM0 RAM
0x3000_0000 | 128 KB | SRAM
0x8000_0000 | 128 KB | DCCM
0xC000_0000 | 32 KB | XCCM
0xE000_0000 | 32 KB | YCCM
0xF000_0000 | 256 Byte | I2S TX
0xF000_1000 | 256 Byte | I2S RX
0xF000_2000 | N/A | Reserved
0xF000_3000 | 256 Byte | BOOT SPI CTRL
0xF000_4000 | N/A | Reserved
0xF000_5000 | 256 Byte | RTC
0xF000_6000 | 256 Byte | PWM
0xF000_7000 | 128 Byte | ADC CTRL
0xF000_8000 | N/A | Reserved
0xF000_9000 | 32 Byte | eFlash CTRL
0xF000_a000 | 144 Byte | SYS Configure
0xF000_b000 | 1 KB | SDIO CTRL
0xF004_0000 | 256 KB | USB CTRL

## Slide 14: Contents
ARC IoT Development Kit
ARC IoT SoC Introduction
On-board Device Introduction
Programmer’s Reference
Getting Started

## Slide 15: Overview of ARC IoT DK
ARC IoT SoC
  EM9D Data Fusion Subsystem
  USB 2.0 OTG, 2x SDIO
  eFLASH (256 KB), SRAM (128 KB)
Memory
  2x SPI Flash (2 MB)
Interfaces
  USB2.0 OTG
  USB Data port (JTAG/UART)
  Micro- SD Card
  9D Sensor (Invensense MPU-9250)
  BTLE module (Microchip RN-4020)
  ADC (16 channels)
  JTAG
  PMIC with dynamic voltage control
Extensions
  Arduino Interface headers
  mikroBUS headers
  Pmod Interfaces (2x)
  Extension header (2x 18 pin)
ARC IoT DK Block Diagram

## Slide 16: Overview of ARC IoT DK
Location of Components On ARC IoTDK

## Slide 17: Configuration Switches and buttons
Configuration Switches to control the board boot and operating mode
FWU switch, used for Firmware Updates, default position: off
  off: Default position. EM9D execute uboot bootloader from embedded flash
  on: Only required if the uboot bootloader residing in the embedded FLASH needs to be updated
Clk32_S switch, used to select the 32.768 KHz clock source
  off: Default position. Setting selects the onboard 32.768 KHz Oscillator
  on: Selects the 32.768 KHz Crystal (and corresponding Xtal I/O Pads)
BSM switch, controls manual or automatic booting of the ARC IoT DK
  off: Default position. Indicates Manual mode. The EM9D only starts booting after the START button is pushed
  on: Selects Automatic mode. The EM9D automatically starts booting after Reset
EXE switch, controls if the EM9D continues with EXEcution or jumps into HALT mode
  off: Default position. Selects EXEcution mode. In case the EM9D continues in EXEcution mode, depending on the FWU switch setting, the Core either continues execution of the Uboot bootloader or starts executing the Firmware Update procedure
  on: Selects HALT mode
The ARC IoTDK includes 3 Buttons: Start, Reset and Wakeup
Start: This button is used to Start the ARC Core if the BSM is in Manual Mode
Reset: Button used to Reset the full board and ARC IoT SoC
Wakeup: Button to wake up the core after the core went in Sleep mode

## Slide 18: ARC IoT Debug Options
USB Data Port
  A USB converter from FTDI (FT2232HL)
  JTAG channel, compatible with MetaWare debugger and GDB
  UART channel, used as console and can be monitored using a standard hyper terminal like PuTTY
6-Pin JTAG Header
  Compatible with the standard Digilent HS1 and HS2 probes
  Ashling Opella XD and Lauterbach Trace-32 probes can be connected via flying leads or by using a 6-pin to 20-pin header converter

## Slide 19: Extension Interfaces
Digilent Pmod™ (2x)
MikroBUS (1x)
Arduino (1x)
2x18 pin extension header

## Slide 20: Digilent Pmod
The ARC IoT DK features two 12-pin Pmod connectors for extension
  The functionality of the Pmod connectors is programmable
  All ports are configured as GPIO after reset
  Detailed pin multiplexer settings are provided in user manual
Pin | GPIO | SPI
A1 | gpio8b_0[0] | spi1_cs_n[0]
A2 | gpio8b_0[1] | spi1_mosi
A3 | gpio8b_0[2] | spi1_miso
A4 | gpio8b_0[3] | spi1_clk
A5 | GND | GND
A6 | 3V3 | 3V3
A7 | gpio8b_0[4] | gpio8b_0[4]
A8 | gpio8b_0[5] | gpio8b_0[5]
A9 | n.c. | n.c.
A10 | n.c. | n.c.
A11 | GND | GND
A12 | 3V3 | 3V3
Pin | GPIO | UART
B1 | gpio8b_1[0] | uart1_cts
B2 | gpio8b_1[1] | uart1_txd
B3 | gpio8b_1[2] | uart1_rxd
B4 | gpio8b_1[3] | uart1_rts
B5 | GND | GND
B6 | 3V3 | 3V3
B7 | gpio8b_1[4] | gpio8b_1[4]
B8 | gpio8b_1[5] | gpio8b_1[5]
B9 | n.c. | n.c.
B10 | n.c. | n.c.
B11 | GND | GND
B12 | 3V3 | 3V3
Pinout Diagram of Pmod
Pmod_B function & Pin assignments
Pmod_C function & Pin assignments

## Slide 21: MikroBUS
The MikroBUS headers enable the addition of Click boards
The Click boards,
  Developed by MikroElektronica: www.mikroe.com, a full list: www.mikroe.com/click
  A range of hundreds of add on boards for interfacing with peripheral sensors and transceivers
  Include wireless and wired connectivity modules, sensor modules, display modules, interface modules, and miscellaneous modules and accessories
MikroBUS I/O Multiplexing
  Multiplexing to get the right function assignment on the MikroBUS headers is controlled by software using the ARDUINO_MUX register
Pin | I/O | MUX Bitfield | Pin | I/O | MUX Bitfield
AN | ADC IN6* | - | PWM | pwm0 | Bit 2
RST | Reset_N | - | INT | gpio4b_2[2] | -
CS | spi2_cs | Bit 1 | RX | uart2_rxd | Bit 0
SCK | spi2_clk | Bit 1 | TX | uart2_txd | Bit 0
MISO | spi2_miso | Bit 1 | SCL | i2c2_scl | Bit 8
MOSI | spi2_mosi | Bit 1 | SDA | i2c2_sda | Bit 8
Pin assignment on the I/O Multiplexer. The “MUX bitfield“ column indicated which bit in the ARDUINO_MUX register is used to control the functionality of this pin

## Slide 22: Arduino
The Arduino shield interface is compatible with the Arduino UNO R3 with the following exceptions:
  5 Volt shields are not supported
  The IOREF voltage is fixed to 3V3
  the ICSP header is also not available
Pin | MUX bitfield | I/O-0 | I/O-1 | I/O-2
AD0 | Bit 10 | ADC IN0 gpio8b_3[7] | - | 
AD1 | Bit 11 | ADC IN1 gpio8b_3[6] | - | 
AD2 | Bit 12 | ADC IN2 gpio8b_3[5] | - | 
AD3 | Bit 13 | ADC IN3 gpio8b_3[4] | - | 
AD4 | Bit 8/Bit 14 | ADC IN4 gpio8b_3[3] | i2c2_sda | 
AD5 | Bit 8/Bit 15 | ADC IN5 gpio8b_3[2] | i2c2_scl | 
IO0 | Bit 0 | gpio4b_2[0] | uart2_rxd | -
IO1 | Bit 0 | gpio4b_2[1] | uart2_txd | -
IO2 | - | gpio4b_2[2] | - | -
IO3 | Bit 2 | gpio4b_2[3] | - | pwm0
IO4 | - | gpio8b_2[0] | - | 
IO5 | Bit 3 | gpio8b_2[1] | - | pwm1
IO6 | Bit 4 | gpio8b_2[2] | - | pwm2
IO7 | - | gpio8b_2[3] | - | -
IO8 | - | gpio8b_2[4] | - | -
IO9 | Bit 5 | gpio8b_2[5] | - | pwm3
IO10 | Bit 1/Bit 6 | gpio8b_2[6] | spi2_cs_n | pwm4
IO11 | Bit 1/Bit 7 | gpio8b_2[7] | spi2_mosi | pwm5
IO12 | Bit 1 | gpio8b_3[0] | spi2_miso | gpio8b_3[0]
IO13 | Bit 1 | gpio8b_3[1] | spi2_clk | gpio8b_3[1]
Pin assignment on the I/O Multiplexer. The “MUX bitfield“ column indicated which bit in the ARDUINO_MUX register is used to control the functionality of this pin

## Slide 23: 2x18 Pin Extension Header
Carried signals in a 2 x 18 pin extension header
  PMOD_A (GPIO, I2C)
  SPI0_slv
  I2S TX and I2S RX
  GPIO4b_1
  I2C0
  SDIO1
  SPI0
The selection of the PMOD_A functionality is controlled by using the PMOD_MUX register

## Slide 24: I2C, SPI, SD, USB
On-board I2C Control Bus
  Controls the on-board MPU-2950 9D sensor (I2C address: 0xD0)
  Is also routed to the 2x18 pin general purpose extension header
SD Card Interface
  Supports SD/SDIO/SDHC/SDXC micro SD cards
  Operates the SD card in the SDR25 speed mode after uboot
USB 2.0 OTG port
  Supports high-speed (480Mbps) transfers using an EHCI host controller
  Supports full (12Mbps) and low (1.5Mbps) speeds through the integrated OHCI host controller
2 x 2 Mbyte SPI Flash
  One SPI Flash (U19, connected to the Boot SPI) is pre-loaded with a firmware upgrade application
  One SPI Flash (U35, connected to SPI master 0) is available for users

## Slide 25: Audio Interface
The ARC IoT DK features stereo I2S interface
  The TX and RX audio signals are available on the 2x18 pin general extension header
  The I2S port operate in master mode, it initializes and drives the I2S select and serial clock signal
  The I2S serial clocks are generated by integer dividers that run at a fixed audio reference clock frequency of 24.576MHz.
  Supported sampling frequencies: 16 KHz, 32 KHz, 48 KHz, 96 KHz, and 192 KHz.
Audio Sample Rate |  |  |  | 
16KHz | 32KHz | 48KHz | 96KHz | 192KHz
24 | 12 | 8 | 4 | 2
I2S SCLK Divider Settings

## Slide 26: ADC
The ARC IoT DK board includes a 16-channel single ended 12-bit ADC Interface
  The analog input range is 0 to 5 Volt
  Channel AD0 – AD5 are available on the Arduino headers
  Channel AD6 – AD15 are available on a dedicated 10-pin header (J2)
  Channel AD6 is also routed to the MikroBUS header AN signal
ADC IN | Usage
0 | Arduino AD0
1 | Arduino AD1
2 | Arduino AD2
3 | Arduino AD3
4 | Arduino AD4
5 | Arduino AD5
6 | mikroBUS AN
6 - 15 | Dedicated header (J2)

## Slide 27: Contents
ARC IoT Development Kit
ARC IoT SoC Introduction
On-board Device Introduction
Programmer’s Reference
Getting Started

## Slide 28: Global Control Registers
SYSCONFIG Control Registers are used to control configuration settings for sub-modules that do not have a software interface
The SYSCONFIG module implements the following functionality
  Logic to sample boot mode configuration values from BOOT pins during power-on-reset
  Logic to generate cpu_start signal for ARC cores
  Logic to generate SW interrupts
Name | Addr offset | Access | Description
Control & Status registers |  |  | 
AHBCLKDIV | 0x04 | RW | AHB clock divisor register
APBCLKDIV | 0x08 | RW | APB clock divisor register
APBCLKEN | 0x0C | RW | APB module clock enable register
CLKODIV | 0x10 | RW | AHB clock output enable and divisor set register
RSTCON | 0x18 | WO | Reset control register
RSTSTAT | 0x1C | RW | Reset status register
AHBCLKDIV_SEL | 0x20 | RW | AHB clock divider select register
CLKSEL | 0x24 | RW | Main clock source select register
PLLSTAT | 0x28 | RO | PLL status register
PLLCON | 0x2C | RW | PLL control register
AHBCLKEN | 0x34 | RW | AHB module clock enable register
I2S_TX_SCLKDIV | 0x40 | RW | I2S TX SCLK divisor register
I2S_RX_SCLKDIV | 0x44 | RW | I2S RX SCLK divisor register
I2S_RX_SCLKSEL | 0x48 | RW | I2S RX SCLK source select register
SDIO_REFCLK_DIV | 0x4C | RW | SDIO reference clock divisor register
GPIO4B_DBCLK_DIV | 0x50 | RW | GPIO4B DBCLK divisor register
SPI_MST_CLKDIV | 0x5C | RW | SPI master clock divisor register
IMAGE_CHK | 0x54 | RO | Image pad status register
PROT_RANGE | 0x58 | RW | PROT range register
PMOD_MUX | 0x70 | RW | PMOD IO multiplex
ARDUINO_MUX | 0x74 | RW | ARDUINO IO multiplex
USBPHY_PLL | 0x78 | RW | USBPHY PLL control register
USBCFG | 0x7C | RW | USB configuration register
TIMER_PAUSE | 0x80 | RW | PWM Timer pause register
GPIO8B_DBCLK_DIV | 0x84 | RW | GPIO8B DBCLK divisor register
UART3SCLK_DIV | 0x8C | RW | Uart3 sclk divider
SYSCONFIG Control Registers Table, base address: 0xF000_a000

## Slide 29: PLL Programming
The PLL inside SYSCONFIG can be re-programmed to a different frequency.
  Switch main clock source to external 16MHz clock
    Write “0” to CLKSEL bit in CLKSEL register
  Update PLL divider settings (N / M / OD / B) in PLLCON register
  Toggle PLL reset for at least 10ns
    write “1” to PLLRST bit in PLLCON register, then write “0” to PLLRST bit
  Wait for PLL lock (implement 0.5ms wait time or poll the PLLSTAT register)
  Switch main clock source to PLL
    Write “1” to CLKSEL bit in CLKSEL register
Typical PLL divider settings
Fin (MHZ) | Fout (MHz) | PLL Divider Settings |  |  | PLLCON Register Settings |  | 
 |  | N | M | NO | R[3:0] | M[13:0] | OD[1:0]
16 | 100 | 1 | 25 | 4 | 1 | 25 | 2
16 | 200 | 1 | 25 | 2 | 1 | 25 | 1
16 | 400 | 1 | 25 | 1 | 1 | 25 | 0

## Slide 30: Simple Application
Application code named myhello.c
Compile your application
ccac myhello.c -av2em -core1 -Os -Hpfnoflt -Hldopt=-Bbase=0x100 -o myhello.elf
Run your application in MetaWare command line mode
mdb -cl -run -hard -digilent myhello.elf
#include "stdio.h"
int main(void) {
printf("Hello world");
return 0;
}
The Hello world message is printed on desktop by MetaWare debugger via a Hostlink interface over a JTAG connection

## Slide 31: Simple Application (2)
Run your application in MetaWare GUI mode
mdb -run -hard -digilent myhello.elf
Set target as following:
Hardware
Digilent Jtag cable
4-wire(standard)

## Slide 32: Contents
ARC IoT Development Kit
ARC IoT SoC Introduction
On-board Device Introduction
Programmer’s Reference
Getting Started

## Slide 33: Getting Started
Installing device drivers
  Digilent Adept tool for ARC JTAG connection and serial debug console
Checking default board settings
  Check if the boot switches and jumpers are set to their default positions
  Use USB cable to connect the USB data port of the ARC IoT DK and host PC
Installing and configuring PuTTY
  PuTTY is a serial console that can be used as a simple debug console
Starting Uboot
  Press the start button on the board for the ARC EM core to start executing the bootloader

## Slide 34: Starting Uboot

## Slide 35: Software & Hands-on Labs
embARC portal
  https://embarc.org
Direct links to the software release of embARC OSP
  https://github.com/foss-for-synopsys-dwc-arc-processors/embarc_osp/releases
Additional documentation on how to get started
  https://github.com/foss-for-synopsys-dwc-arc-processors/ARC-Development-Systems-Forum/wiki/ARC-Development-Systems-Forum-Wiki-Home
Hands-on labs source code & handbook
  https://github.com/foss-for-synopsys-dwc-arc-processors/arc_labs/tree/master/labs
  https://embarc.org/arc_labs/doc/build/html/index.html