## Slide 1: DSP Processors Solutions
DSP Bottleneck | Solution
Most operations are multiplications followed by addition of result (accumulation) | Hardware Multiply accumulate operations (MAC)
Complex, Vecto,r and Matrix Operations spend much CPU time | Special Matrix, Vector, and Complex operations
Overflow creates invalid data | Hardware support for managing arithmetic computation (Shifters and Guard bits to prevent overflow) + Fixed point data (Saturation, instead of overflow)
CPU time spent counting and comparing loop variable | Hardware looping
CPU time spent accessing memory | Special low-latency memory
CPU time spent calculating next memory addresses | Special address generation units (AGU) in parallel to processing

## Slide 2: Fused Instructions, Higher Performance, Smaller Code Size
Fusing of memory accesses, arithmetic operations into one instruction
  Load two source operands (one from X memory and one from Y memory) from XY memory by dereferencing address pointers
  Post-increment the address pointers
  Compute the result of the instruction (multiply the operands, MAC the operands, and so on)
  Write back the result to XY memory by de-referencing an address pointer
  Post-increment the destination address pointer
Without AGU memory:
ld ra, [addr1]
ld rb, [addr2]
add rc, ra, rb
st rc, [addr3]
add addr1, x
add addr2, y
add addr3, z
With AGU memory:
add %agu_u2, %agu_u1, %agu_u0
7 instructions fused into 1
CCM Memories
Greatly reduces instruction count, memory accesses
Optimal performance for DSP kernel tasks
Greatly reduces required cycle count
Notes: Benefit of fused instructions is a smaller instruction footprint, higher computation performance and lower power

## Slide 3: DSP Library
DSP library is supplied with source code with MetaWare Development Toolkit
Includes the following groups of functions:
  Fast Math Functions Cosine, sine, square-root, atan2, base 2 logarithm, base 2 exponent, reciprocal, fractional division
  Vector Math Functions Addition, subtraction, offset, absolute value, negation, shift, multiplication, scale, dotproduct, vector minimum and vector maximum
  Complex Math Functions Conjugate, dot product, magnitude, magnitude squared, complex multiply by complex, complex multiply by real
  Filtering Functions Convolutions, correlation, real/complex FIR filters, FIR decimator, FIR interpolator, adaptive LMS FIR filter, direct form 1/2 type IIR filters, IIR lattice filter
  Matrix Math Functions Initialization, addition, subtraction, multiplication, transportation, scaling, inversion
  Interpolation Functions Linear interpolation, bilinear interpolation, polynomial evaluation
  Fast Transform Functions Complex FFT/iFFT, Real FFT/iFFT, DCT2, DCT3, DCT4, MDCT/iMDCT
The software functions support single-precision floating-point (float f32)
and fixed-point data formats (q31, q15, q7, v2q15, cq15)